## Slide 1: Chromatography
Thin Layer Chromatography - t.l.c
Gas - Liquid Chromatography G.l.c

## Slide 2: The general principle
Use – to separate and identify components of mixtures.
Several different types - paper, thin layer, gas-liquid.
All use the principle of “partition” - affinity between two phases, to separate mixtures of substances.
Stationary phase & mobile phase.
Compounds with greatest affinity for mobile phase travel further.

## Slide 3: Thin Layer Chromatography - t.l.c.
Series of spots forms
Compare samples in mixture with known substances.
Measure Rf values.
Coloured compounds & colourless compounds.

## Slide 4: Separation and identification.

## Slide 5: Gas - Liquid Chromatography G.l.c.
Sample introduced by syringe.
Column separates components.
(Heated in oven)
Detector monitors compounds emerging from outlet.
Recorder plots signals as a chromatogram.

## Slide 6: What happens in practice.
Compounds that have high affinity for mobile phase emerge first, (most volatile).
Chromatogram charts recorder response against time.
Each component - separate peak.
Retention time – characteristic of the compound under given conditions.

## Slide 7: Factors affecting retention time:
length of column
packing material
type of carrier gas
flow rate of carrier gas
temperature of column.

## Slide 8: Interpreting the trace
Calibration – known compounds are added to the column and conditions kept constant.
Amount of substance – area under peak / peak height.
Relative proportions can be determined.

## Slide 9: Uses of G.l.c.
Very sensitive - small quantities of substances detected, explosives, drugs etc.
Separation of pure substances for collection.
Can be connected to mass spectrometer for direct identification of substances.