## Slide 1: Polymers

## Slide 2: What is a polymer?
A long molecule made up from lots of small molecules called
monomers.

## Slide 3: Addition polymerisation
Monomers contain C=C bonds
Double bond opens to (link) bond to next monomer molecule
Chain forms when same basic unit is repeated over and over.
Modern polymers also developed based on alkynes R-C C - R’

## Slide 4: Copolymerisation
when more than one monomer is used.
An irregular chain structure will result eg propene/ethene/propene/propene/ethene
Why might polymers designers want to design a polymer in this way?
(Hint) Intermolecular bonds!

## Slide 5: What decides the properties of a polymer?
Stronger attractive forces between chains = stronger, less flexible polymer.
Chains able to slide past each other = flexible polymer .
In poly(ethene) attractive forces are weak instantaneous dipole - induced dipole, will it be flexible or not?
Nylon has strong hydrogen bonds, why does this make it a strong fibre?

## Slide 6: Getting ideas straight
Look at page 110 -111 of Chemical Ideas.
Take turns in explaining to a partner how the following molecular structures affect the overall properties of polymers :-
chain length, different side groups, chain branching, stereoregularity, chain flexibility, cross linking.

## Slide 7: Thermoplastics (80%)
No cross links between chains.
Weak attractive forces between chains broken by warming.
Change shape - can be remoulded.
Weak forces reform in new shape when cold.

## Slide 8: Thermosets
Extensive cross-linking formed by covalent bonds.
Bonds prevent chains moving relative to each other.
What will the properties of this type of plastic be like?